ype	How to Add	Nickname Example	Path Example
Symbol	Preferences → Manage Symbols	MyComponents	D:/KiCad_Libraries/MySymbols.kicad_sym
Footprint	Preferences → Manage Footprints	MyFootprints_USB	D:/KiCad_Libraries/MyFootprints.pretty
3D Models	In Footprint Properties	TPD2EUSB30ADRTR	D:/KiCad_Libraries/3DModels/TPD2EUSB30ADRTR.step

Pin Group	Action
D+ / D− (pairs)	Merge → USB_DP_PROT, USB_DM_PROT
CC1 / CC2	5.1kΩ to GND
GND / Shield	Tie to common ground
VBUS	Connect if USB-powered
SBU, RX/TX SuperSpeed lines	Leave unconnected

ESD diode (TPD2EUSB30ADRTR):
- Pin 1 → USB_DP_PROT
- Pin 3 → USB_DM_PROT
- Pin 2 → GND

CH340G Pin	ESP32 Connection	Notes
TXD	→ RXD0 (IO3)	Serial TX → MCU RX
RXD	← TXD0 (IO1)	Serial RX ← MCU TX
DTR	→ EN via 0.1µF + diode
RTS	→ IO0 via 0.1µF + diode
UD+/−	← USB D+/D− via ESD
VCC	← 3.3V	Power
GND	← GND	Ground
Others	NC	Ignore CTS, DCD, RI, etc.

RTS ──┬─ 0.1µF ──► IO0
      └─ 1N4148W

DTR ──┬─ 0.1µF ──► EN
      └─ 1N4148W

EN ──► 10kΩ to +3.3V
EN ──► Button → GND
EN ──► 1µF to GND
IO0 ──► 10kΩ to GND
A second view of the above.
[ Reset Button ]
EN ───┬────► 10kΩ ───► +3.3V
      └────► Push Button ───► GND
      └────► 1µF to GND

[ Boot Button ]
IO0 ───┬────► 10kΩ ───► +3.3V
       └────► Push Button ───► GND

Action	Shortcut
3D Preview	Alt+3
ERC / DRC	F8 / F9
Footprint Assignment	Post-schematic
Show Pads	View → Show Pad Numbers
Net Inspector	Inspect → Nets

### Modular Block Strategy
- Create sub-sheets for CH340 ↔ USB-C ↔ ESP32
- Use clear net names: UART_TX_CH340, USB_DP_PROT, RTS_RESET
- Label unused pins as NC for clarity
- Store blocks in a folder like RickBlocks or RickLibrary
*****************************************************************************
Wire.begin(18, 13); // SDA = GPIO18, SCL = GPIO13
Wire.begin(); // SDA = GPIO21, SCL = GPIO22